## Slide 1: Introduction to RT Component Creation
Nobuhiko Miyamoto
National Institute of Advanced Industrial Science and Technology
Industrial Cyber-Physical Systems Research Center
Software Platform Research Team
Notes: Now, let's start "Part 2 Introduction to RT Component Creation".

## Slide 2: If you have any questions
2
Ask a question in Zoom’s chat.
Display the Zoom Group Chat screen
If the problem is not solved by chat, we will provide individual support.
Please set the destination to everyone.
Notes: 2
If you have any questions, please use Zoom’s chat.
If the problem is not solved by chat, we will provide individual support.

## Slide 3: Document
3
Please, open the following WEB site.
Windows
  https://openrtm.org/openrtm/ja/doc/casestudy/raspberrypi_mouse/raspimouse_tutorial_rtm_seminar/tutorial_rtm_seminar_win_part2
Ubuntu
  https://openrtm.org/openrtm/ja/doc/casestudy/raspberrypi_mouse/raspimouse_tutorial_rtm_seminar/tutorial_rtm_seminar_ubuntu_part2
Notes: 3
Please, open the following WEB page.
Send the URL in chat.

## Slide 4: Outline of the training
4
Creating component to operate the mobile robot (Raspberry Pi Mouse) on the simulator.
  Target speed input by GUI
  Stops when the sensor value exceeds a certain level
Notes: 4
In this training, Let’s try creating an RTComponent to control a mobile robot on the simulator.
The Robot Controller Component commands the mobile robot to speed by GUI.
Also, the mobile robot should stop according to the value of the distance sensor.

## Slide 5: Raspberry Pi Mouse Overview
5
Raspberry Pi Mouse is an two-wheel drive mobile robot sold by RT.
Distance sensor
Drive wheels
Front
Back
Notes: 5
Raspberry Pi Mouse is an two-wheel drive mobile robot sold by RT.
Raspberry Pi mouse has four distance sensors on the front.

## Slide 6: The procedure of the training
6
Creating a template for source code using RTC Builder
Edit source code and build.
  Generate various files required for build
    Various files generated by CMake
  Editing source code
    Editing RobotController.h and RobotController.cpp
  Build
    Visual Studio、Code::Blocks
RT System creation and operation check using RT System Editor
  RT system creation
    Data port connection, configuration parameter settings.
Notes: 6
The procedure of the training is like this.
First, use RTC Builder to generate a source code template.
Second, edit the source code and build.
Finally, use RTSystemEditor to build the RT system and check its operation.

## Slide 7
Component development tools
RTC Builder
Notes: Now let's talk about the component development tool RTC Builder.

## Slide 8: RTC Builder
8
A tool that enters component profile information and generates a template such as source code
  Output C ++, Python, Java, Lua source code
Notes: 8
RTCBuilder is a tool that can output template code by inputting the profile information of the component.

## Slide 9: Launch RTC Builder
9
Steps to start RTC Builder
  Windows(OpenRTM-aist 1.2)
    Double-click on the desktop shortcut
  Ubuntu
    Enter the following command
    $ openrtp
Notes: 9
Now, I will explain the procedure to start RTC Builder.
If you are using Windows, double-click on the desktop shortcut.
If you are using Ubuntu, enter the command "openrtp".

## Slide 10: Start RTC Builder
10
Set any location in the workspace and click Launch.
The Welcome page opens when you first start OpenRTP, so close it.
Notes: 10
When the "Eclipse Lancher" screen opens, set any location in the workspace and click Launch.
日本語環境の場合は起動ボタンを押す。
The Welcome page opens when you first start OpenRTP, so close it.

## Slide 11: Start RTC Builder
11
Click the "Open Perspective" button.
select "RTC Builder" and click the Open button.
Notes: 11
Then click the "Open Perspective" button.
When the "Open Perspective" screen is displayed, select "RTC Builder" and click the Open button.
日本語環境の場合は開くボタンを押す。

## Slide 12: Project creation
12
Create skeleton code for the RobotController component.
  Wheel type mobile robot operation component
    Operate the robot with GUI
    Stops when the sensor value exceeds a certain level
Notes: 12
First, let’s create a Robot Controller Component project.

## Slide 13: Project creation
13
A folder called "RobotController" is created in the directory specified in the workspace when Eclipse starts.
  At this point, only "RTC.xml" and ".project" are generated
The following items will be set
  Basic profile
  Activity profile
  Data port profile
  Service port profile
  configuration
  document
  Language environment
  RTC.xml
Click the icon below
Set "Robot Controller" to the project name and click finish.
Notes: 13
Please click this icon.
When the "RTC Builder Project" screen is displayed, enter "Robot Controller" in the project name and click the finish button.
日本語環境では終了。
Then, the project is generated in the folder in the workspace.

## Slide 14: Enter basic profile
14
Set basic component information such as RT component profile information.
Code generation, import/export, packaging process
RTC profile editor
Enter each item here
Hint
Select the Basic tab.
Notes: 14
Please, select the Basic tab.
日本語は基本タブ。
From now on, you will enter basic information such as component names.

## Slide 15: Enter basic profile
15
Component name
  RobotController
Module overview
  Optional (Robot Controller Component)
version
  Optional (1.0.0)
Vendor name
  Any
Module category
  Optional (Controller)
Component type
  STATIC
Activity type
  PERIODIC
Component type
  DataFlow
Maximum number of instances
  1
Execution type
  PeriodicExecutionContext
Execution cycle
  1000.0
Overview
  Any
Notes: 15
Please, set "Robot Controller" for the component name.
This is the only setting item on the basic tab.
日本語環境はコンポーネント名。

## Slide 16: Activity settings
Steps to enable specified activity
Set the activity to use.
Select the Activity tab.
Activated activity names have a blue background
1. Select the activity name you want to use or not use
(Displayed in red when selected)
2. After selecting the activity name, select ON-OFF.
Notes: 16
Please, select the Activity tab.
This section describes how to set enabling the specified activity.
At first, Select the activity name you want to use or not use.
Second, After selecting the activity name, select ON-OFF.
Enabled activity names have a blue background.

## Slide 17: Activity settings
17
コールバック関数 | 処理
onInitialize | Initialization process
onActivated | Called only once when activated
onExecute | Called periodically when active
onDeactivated | Called only once when deactivated
onAborting | Called only once before entering ERROR state
onReset | Called only once when reset
onError | Called periodically in ERROR state
onFinalize | Called only once at the end
onStateUpdate | Called every time after onExecute
onRateChanged | Called only once when the ExecutionContext rate changes
onStartup | Called only once when ExecutionContext starts execution
onShutdown | Called only once when ExecutionContext stops executing
Notes: 17

## Slide 18: Activity settings
18
Enable the following activities
  onInitialize
  onActivated
  onDeactivated
  onExecute
Notes: 18
Please, Enable the onActivated, onDeactivated, and onExecute activities.

## Slide 19: Data port settings
Steps to add a data port
Add and set InPort and OutPort
Select the Data Port tab.
Click the add button for ImPort or OutPort.
Click the port name to rename it.
Set each item.
Notes: 19
Please, select the Data Port tab.
This section describes the procedure for adding a data port.
At first, click the add button for ImPort or OutPort.
Next, Click the port name to rename it.
Finaly, set items such as data type.

## Slide 20: Data port settings
Set the following InPort
  in
    Data Type： RTC::TimedShortSeq
    Please do not mistake it for TimedShort type.
Set the following OutPort
  out
    Data Type ： RTC::TimedVelocity2D
    Please do not mistake it for TimedVelocity3D type and TimedVector2D.
Select the data type from the drop-down list.
Notes: 20
At first, add InPort, please.
Set the port name to "in“.
Set the data type to RTC::TimedShortSeq.
Second, add OutPort, please.
Set the port name to “out".
Set the data type to RTC::TimedVelocity2D.

## Slide 21: About the data port
Port for communicating continuous data
以下の例はデータフロー型がpush、サブスクリプション型がflush、インターフェース型がcorba_cdrの場合
Notes: 21

## Slide 22: About RTC::TimedVelocity2D type
Data type for expressing the speed of a mobile robot defined in ExtendedDataTypes.idl.
  vx: Velocity in the X-axis direction
  vy: Velocity in the Y-axis direction (0 assuming the wheels do not skid)
  va: Angular velocity around the Z axis
Set straight speed with vx and rotation speed with va
Notes: 22
By the way, TimedVelocity2D type is a data type that represents the speed of a mobile robot.
This data type can be set to translation speed vx, vy and rotation speed va.

## Slide 23: Configuration Parameter settings
Steps to add configuration parameters
Add and set configuration parameters
Select the Configuration tab.
Click the add button.
Click the parameter name to rename it.
Set each item.
Notes: 23
Please, select the Data Port tab.
This section describes the procedure for adding a configuration parameter.
At first, click the add button.
Next, Click the parameter name to rename it.
Finaly, set items such as data type.

## Slide 24: Configuration Parameter settings
Set the following configuration parameters
  speed_x
    Type：double
    Default Value： 0.0
    Constraint：-1.5<x<1.5
    Widget：slider
    Step: 0.01
  speed_r
    Type：double
    Default Value： 0.0
    Constraint ：-2.0<x<2.0
    Widget：slider
    Step: 0.01
Enable operation of mobile robots using GUI (slider)
Notes: 24
Add these configuration parameters, please.
The parameters of speed_x are Type is double, Default Value is 0.0, Constraint is -1.5 to 1.5 range, Widget is slider, and Step is 0.01.
The parameters of speed_r are Type is double, Default Value is 0.0, Constraint is -2.0 to 2.0 range, Widget is slider, and Step is 0.01.
Type：データ型
Constraint：制約条件

## Slide 25: Configuration parameter constraints, and widget settings
Constraint：0<=x<=100
Widget：slider
Step：10
Constraint：0<=x<=100
Widget：spin
Step：10
Widget：text
Show GUI when editing configuration parameters in RT System Editor
Notes: 25

## Slide 26: Configuration parameter constraints, and widget settings
Constraint：(0,1,2,3)
Widget：checkbox
Constraint：(0,1,2,3)
Widget：ordered_list
Constraint：(0,1,2,3)
Widget：radio
Notes: 26

## Slide 27: Configuration Parameter settings
Set the following configuration parameters
  stop_d
    Type：int
    Default Value： 30
Stop when the sensor value is
greater than or equal to this value
Notes: 27
Add configuration parameters of stop_d, please.
The parameters of stop_d are Type is int, Default Value is 0.0, Constraint is -1.5 to 1.5 range, Widget is slider, and Step is 0.01.

## Slide 28: Raspberry Pi mouse distance sensor
Raspberry Pi mouse is equipped with a distance sensor
  The measured value becomes larger as the distance to the object is shorter.
The simulator also calculates and outputs a value close to this data.
Notes: 28

## Slide 29: ドキュメントの設定
各種ドキュメント情報を設定
今回は適当に設定しておいてください。
  空白でも大丈夫です
Notes: 29

## Slide 30: Language setting
Set information about the language to be implemented and the operating environment.
Set the language.
This time, set "C ++".
Select the Language and Environment tab.
Notes: 30
Please, select the Language and Environment tab.
Set the language to C ++, Please.
日本語環境：言語・環境

## Slide 31: Skeleton code generation
A skeleton code is generated by pressing the code generation button from the basic tab.
  Workspace\RobotController
    Source code
      C++ Source files(.cpp)
      Header files (.h)
    CMakeLists.txt
    rtc.conf、RobotController.conf
    etc.
Check the generated file
  Right-click the created project and select “Show In“(表示方法)-> "System Explorer".
  Explorer will open the workspace folder, so check if the above file exists
Select the Basic tab.
Click the code generation button
Right click on the created project
“Show In”-> “System Explorer”
Notes: 31
Now let's generate skelton code.
Please, Select the Basic tab and click the code generation button.
Please, Check the generated file.
日本語環境：コード生成ボタン
Show In：表示方法

## Slide 32
Edit source code, build RTC
Notes: In this chapter, I will explain how to edit and build the source code.

## Slide 33: Steps to build
33
Generate various files required for build
  Various files generated by CMake
Edit the source code
  Edit RobotController.h
  Edit RobotController.cpp
Build
  Windows： Visual Studio
  Ubuntu： Code::Blocks
Notes: 33
This section describes the procedure up to the build execution.
At first, generate various files required for build by CMake.
Second, edit source code.
Finaly, run the build.

## Slide 34: CMake
34
Generate various files required for build
  Describe the settings in CMakeLists.txt.
    CMakeLists.txt is also generated when you create the skeleton code in RTC Build
Notes: 34

## Slide 35: Generating files needed for build
35
Start CMake
  Windows 7
    「スタート」→「すべてのプログラム」→「CMake」→「CMake (cmake-gui)」
  Windows 8.1
    「スタート」→「アプリビュー(右下矢印)」→「CMake」→「CMake (cmake-gui)」
  Windows 10
    左下の「ここに入力して検索」にCMakeと入力して表示されたCMake(cmake-gui)を起動
  Ubuntu
    Enter the following command
    cmake-gui
Notes: 35
Start CMake-gui, please.
If you are using Ubuntu, type "cmake-gui".

## Slide 36: cmake-guiの起動
36
Windows 8.1
デスクトップ
スタート画面
アプリビュー
Notes: 36

## Slide 37
37
Windows 10
cmake-guiの起動
Enter "cmake" in "ここに入力して検索" at the bottom left
Notes: 37
If you are using Windows 10, search for cmake, please.

## Slide 38: Generating files needed for build
38
Drag and drop CMakeLists.txt onto cmake-gui
  CMakeLists.txt is a folder for projects generated by RTC Builder.
  (例： C:\workspace\RobotController)
Notes: 38
Drag and drop CMakeLists.txt onto cmake-gui, please.
CMakeLists.txt is in the workspace project.

## Slide 39: Generating files needed for build
39
Set the folder to generate solution files etc.
(e.g.:C:/workspace/RobotController/build)
Add "/build" after drag and drop.
Notes: 39
Please set the item of "Where to build the binaries".
"Where to build the binaries" sets the path of "Where is the source code" with "/build" added.

## Slide 40: ビルドに必要なファイルの生成
40
Click the Configure button.
Collect library information required for compilation.
Select YES
Notes: 40
Click the Configure button, please.

## Slide 41: For CMake 3.14 or later
41
Build environment settings
Visual Studio 2017 → Visual Studio 15 2017
Visual Studio 2013 → Visual Studio 12 2013
Code::Blocks → CodeBlocks-Unix Makefiles
Select X64.
After setting, press the Finish button.
Notes: 41
The setting procedure when CMake is 3.14 or later is as shown in the slide.

## Slide 42: CMake 3.13以前の場合
42
Notes: 42

## Slide 43: Generating files needed for build
43
If "Configure done" is displayed, it is successful.
Notes: 43
If "Configure done" is displayed, it is successful.
If you get an error, please use chat.

## Slide 44: Generating files needed for build
44
Click the Generate button to generate the file.
If "Generating done" is displayed, it is successful.
Notes: 44
Click the Genarate button, please.
If "Generating done" is displayed, it is successful.

## Slide 45: Editing source code
45
Click the "Open Project" button to start Visual Studio.
Notes: 45
Click the "Open Project“ button, please.

## Slide 46: Editing source code
46
If the version of CMake-gui is old, there is no "Open Project" button, so double-click the file to open it.
  Windows
    le-click "RobotController.sln" in the build folder to open it
  Ubuntu
    Double-click "RobotController.cbp" in the build folder to open it.
Notes: 46

## Slide 47: Editing source code
47
Windows
  Visual Studio starts
Ubuntu
  Code::Blocks starts
Notes: 47
Visual Studio will start if you are using Windows, and Code::Blocks will start if you are using Ubuntu.

## Slide 48: Editing source code
48
Edit RobotController.h
Visual Studio
Code::Blocks
Open RobotController.h from Solution Explorer
Notes: 48
Open RobotController.h from Solution Explorer, Please.

## Slide 49: Editing source code
49
Edit RobotController.h
Declaration of a variable that temporarily stores the sensor value
int sensor_data[4];
Notes: 49
Please, edit RobotController.h.
Declare a variable to store the sensor value.

## Slide 50: Editing source code
50
Edit RobotController.cpp
Visual Studio
Code::Blocks
Open RobotController.cpp from Solution Explorer
Notes: 50
Open RobotController.cpp from Solution Explorer, Please.

## Slide 51: Editing source code
51
Edit RobotController.cpp
Added to onActivated function
Added to onDeativated function
Notes: 51
Please, edit RobotController.cpp.
Edit the onActivated function and onDeactivated function like this.

## Slide 52: Editing source code
52
Edit RobotController.cpp
  If it is difficult to write, please copy and paste from the following page.
  https://openrtm.org/openrtm/ja/node/6550#toc20
Added to onExecute function
Notes: 52
Edit the onExecute function like this.

## Slide 53: Editing source code
53
Procedure to read data
Check if there is newly written data with the isNew function
Read data with read function
Data is stored in the variable m_in when the read function is called.
TimedShortSeq type holds multiple data like an array.
Notes: 53
This section describes the procedure for reading data.
At fitst, Check if there is newly written data with the isNew function.
Second, Read data with read function.
Finaly, Data is stored in the variable m_in when the read function is called.

## Slide 54: Editing source code
54
Procedure for writing data
Store data in the variable m_out.
Since it is a TimedVelocity2D type, the straight speed is stored in vx and the rotation speed is stored in va.
Write data with write function
When the configuration parameter is changed, the value is stored in the corresponding variable (m_speed_x, m_speed_r, m_stop_d).
Notes: 54
This section describes the procedure for writing data.At first, Store data in the variable m_out.
Next, Write data with write function.

## Slide 55: RTC build
55
Visual Studio
Code::Blocks
  If successful, an executable file will be generated.
    Windows
      RobotControllerComp.exe is generated in the Release (or Debug) folder of the build\src folder.
    Ubuntu
      RobotControllerComp is generated in the build/src folder
Notes: 55
Please, Compile the source code.

## Slide 56
System construction support tool
RT System Editor
Notes: Now let's talk about the System construction support tool RTC System Editor.

## Slide 57: RT System Editor
57
Tool for operating RTC with GUI
  Data port and service port connection
  Activate, deactivate, reset, exit
  Manipulating configuration parameters
  Manipulating the execution context
    Change execution cycle
    Execution context association
  Composite
  Launch RTC from manager
  Save and restore the created RT system
Notes: 57
RT System Editor is Tool for operating RTC with GUI.
You can connect data ports and activate the RTC on the GUI.

## Slide 58: Start RTSystemEditor
58
Click the "Open Perspective" button.
select "RTSystemEditor" and click the Open button.
Notes: 58
Then click the "Open Perspective" button.
When the "Open Perspective" screen is displayed, select "RTSystemEditor" and click the Open button.
日本語環境の場合は開くボタンを押す。

## Slide 59: RT System Editor screen configuration
59
Notes: 59
The screen configuration of RT System Editor is like this.

## Slide 60: Operation check of RobotController component
60
Create an RT system that connects to simulator components and operates robots on the simulator
  Start Naming Service
  Start RaspberryPiMouseSimulator Component
    Windows
      In the EXE folder of the extracted ZIP file
      Double-click "RaspberryPiMouseSimulatorComp.exe"
    Ubuntu
      If not installed
        $ wget https://raw.githubusercontent.com/OpenRTM/RTM_Tutorial_ROBOMECH2019/master/script/install_raspimouse_simulator.sh
        $ sh install_raspimouse_simulator.sh
      Go to the RasPiMouseSimulatorRTC directory and enter the following command
        $ build/src/RaspberryPiMouseSimulatorComp
  Start RobotController Component
  Connect the RaspberryPiMouseSimulator component and RobotController component and execute "All Activate"
Notes: 60
From now on, Let’s try checking the operation of the RobotController component.
At First, start the simulator component.
Second, Start RobotController Component.
Finally, Connect Connect the RaspberryPiMouseSimulator component and RobotController component and execute "All Activate“.

## Slide 61: Naming Service
61
A service that manages objects by name
  Register the RTC with a unique name
    Tools such as RT System Editor get object references by name from the name server
Procedure to start
Click the “Start_NameService" button.
If "localhost" is added to the left view, it is successful.
Notes: 61
Naming Service is A service that manages objects by name.
Please, start Naming Service.
At First, click the “Start_NameService" button.
If "localhost" is added to the left view, it is successful.

## Slide 62: Start Naming Service
62
OpenRTM-aist 1.1.2以前の手順
  Windows 7
    「スタート」→「すべてのプログラム」→「OpenRTM-aist 1.2.0」→「Tools」→「Start Naming Service」
  Windows 8.1
    「スタート」→「アプリビュー(右下矢印)」→「OpenRTM-aist 1.2.0」→「Start Naming Service」
  Windows 10
    左下の「ここに入力して検索」にStart Naming Serviceと入力して起動
  Ubuntu
    $ rtm-naming
Notes: 62

## Slide 63: Operation check of RobotController component
63
Create an RT system that connects to simulator components and operates robots on the simulator
  Start Naming Service
  Start RaspberryPiMouseSimulator Component
    Windows
      In the EXE folder of the extracted ZIP file
      Double-click "RaspberryPiMouseSimulatorComp.exe"
    Ubuntu
      If not installed
        $ wget https://raw.githubusercontent.com/OpenRTM/RTM_Tutorial_ROBOMECH2019/master/script/install_raspimouse_simulator.sh
        $ sh install_raspimouse_simulator.sh
      Go to the RasPiMouseSimulatorRTC directory and enter the following command
        $ build/src/RaspberryPiMouseSimulatorComp
  Start RobotController Component
  Connect the RaspberryPiMouseSimulator component and RobotController component and execute "All Activate"
Notes: 63
Please, start RaspberryPiMouseSimulator Component.
RaspberryPiMouseSimulatorComp.exe is in the ZIP file.
Please, Double-click "RaspberryPiMouseSimulatorComp.exe“.
If you are using Ubuntu, enter these commands.
Next, start Robot Controller Component.
Please, execute RobotControllerCOmpo.exe.

## Slide 64: Data port connection
Clicking this button launches System Diagram.
Drag and drop RaspberryPiouseSimulator0.rtc and RobotController0.rtc from the name service view on the left to the System Diagram.
Notes: 64
From now on, connect the data port and check the operation.
Please, click this button to open the system diagram.
Please, Drag and drop RaspberryPiouseSimulator0.rtc and RobotController0.rtc from the name service view on the left to the System Diagram.

## Slide 65: Data port connection
Drag and drop "out" of RobotController0 to "target_velocity_in" of RaspberryPiMouseSimulator0
Click the OK button.
1. A line appears between the ports
2. InPort and OutPort are displayed in green
Notes: 65
Please, Drag and drop "out" of RobotController0 to "target_velocity_in" of RaspberryPiMouseSimulator0.
Click the OK button on the Connector Profile screen, please.
When the ports are connected, a line appears between the ports.

## Slide 66: Data port connectionの接続
Connect "ir_sensor_out" of RaspberryPiSimulator0 and "in" of RobotController0.
Notes: 66
Please, connect "ir_sensor_out" of RaspberryPiSimulator0 and "in" of RobotController0.

## Slide 67: Activation
If the button does not appear, restart OpenRTP.
Exit OpenRTP.
Double-click on the shortcut.
Click the Activate Systems button.
If the RTC changes green, activation is successful.
Notes: 67
From now on, let’s try activating the RTC.
Please, click the Activate Systems button.
If the RTC changes green, activation is successful.
If the button does not appear, restart OpenRTP.

## Slide 68: Change configuration parameters
68
Change configuration parameters using RT System Editor
Check if the following operations can be performed
  Can the robot on the simulator be operated with the slider?
  Does the robot stop when it approaches an wall?
1. Click RobotController0.
2. Click the edit button.
Operate with the slider.
Notes: 68
Let's change the configuration parameters from the RTSystemEditor.
At first, click RobotController0.
Second, click the edit button.
Finally, Operate with the slider.
Please, Please check the operation.
Edit：編集

## Slide 69: 動作確認
69
When it stops when the wall approaches the distance sensor
When the wall does not stop when approaching the distance sensor
Advance to the wall
Stop in front of the wall
Continue to move forward even after touching the wall
Notes: 69
Please, Check if the robot stops in front of the wall.

## Slide 70: RTコンポーネントの状態遷移
RTCには以下の状態が存在する
  Created
    生成状態
    実行コンテキストを生成し、start()が呼ばれて実行コンテキストのスレッドが実行中(Runnning)状態になる
    自動的にInactive状態に遷移する
  Inactive
    非活性状態
    activate_componentメソッドを呼び出すと活性状態に遷移する
    RT System Editor上での表示は青
  Active
    活性状態
    onExecuteコールバックが実行コンテキストにより実行される
    リターンコードがRTC_OK以外の場合はエラー状態に遷移する
    RT System Editor上での表示は緑
  Error
    エラー状態
    onErrorコールバックが実行コンテキストにより実行される
    reset_componentメソッドを呼び出すと非活性状態に遷移する
    RT System Editor上での表示は赤
  終了状態
Notes: 70
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 71: RTコンポーネントの状態遷移(生成直後)
Notes: 71
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 72: RTコンポーネントの状態遷移(アクティブ化)
Notes: 72
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 73: システムの保存
Notes: 73
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 74: システムの復元
以下の内容を復元
  ポート間の接続
  コンフィギュレーション
  「Open and Create Restore」を選択した場合はマネージャからコンポーネント起動
Notes: 74
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 75: 非アクティブ化、終了
非アクティブ化
終了
Notes: 75
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 76: RTコンポーネントの状態遷移(非アクティブ化)
Notes: 76
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 77: Raspberry Piマウス実機との接続
Raspberry PiとノートPCを無線LANで接続
  Raspberry Piが無線LANアクセスポイントになる
注意事項
  ノートPCに複数のネットワークインターフェースが存在する場合にRTCの通信ができなくなる可能性があります。
    問題が発生した場合は個別に対応します。
  Raspberry Piアクセスポイント接続後はインターネットに接続できなくなります。
  Raspberry Piアクセスポイント接続後に、起動済みのネームサーバーとRTCは再起動してください。
  Raspberry Piはシャットダウンしてから電源スイッチをオフにするようにしてください
  モーター電源スイッチはこまめに切るようにしてください
Notes: 77
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 78: Raspberry Piとの接続
Raspberry Piの電源投入
  内側のスイッチをオンにする
電源を切る場合
  3つ並んだスイッチの中央のボタンを1秒以上押す
  10秒ほどでシャットダウンするため、その後に電源スイッチをオフにする
Notes: 78
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 79: Raspberry Piとの接続
無線LANアクセスポイントとの接続
  SSID、パスワードはRaspberry Piマウス上のシールに記載
  接続手順(Windows)
    画面右下のネットワークアイコンをクリック
    raspberrypi_xxに接続後、パスワードを入力
Notes: 79
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 80: ネームサーバーとの接続
Notes: 80
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 81: 起動済みのRTC、ネームサーバー再起動
ネームサーバーを再起動する
  OpenRTM-aist 1.2の場合はネームサーバー起動ボタンで再起動
  OpenRTM-aist 1.1.2の場合はネームサーバーのプロセス終了後、「Start Naming Service」を再度実行
RTC再起動
  RTCをexitするか、RTC起動時に表示したウインドウの×ボタンを押して終了する
  実行ファイル(RobotControllerComp.exe)を再度実行
Notes: 81
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 82: ポートの接続
RobotController0とRapberryPiMouseRTC0を接続する
Notes: 82
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 83: 動作確認
モーターの電源投入
  外側のスイッチをONにする
RTCをアクティブ化して動作確認
Notes: 83
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 84: リセット
RTCがエラー状態に遷移した場合にエディタ上には赤く表示される。
以下の操作で非アクティブ状態に戻す
Notes: 84
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 85: RTコンポーネントの状態遷移(エラー)
Notes: 85
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 86: RTコンポーネントの状態遷移(リセット)
Notes: 86
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 87
RTC Builder
補足

## Slide 88: サービスポートの設定
サービスポートの追加、インターフェースの追加、設定を行う
Notes: 88
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 89: サービスポートの設定
インターフェースを追加する
Notes: 89
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 90: サービスポートの設定
コード生成後、Pythonの場合はidlcompile.bat(idlcompile.sh)を起動する
インターフェースの設定を行う
Notes: 90
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 91: サービスポートの設定
IDLファイルについて
  プログラミング言語に非依存のインターフェース定義言語
コンシュマー側でプロバイダ側のecho、get_valueなどのオペレーションを呼び出す
Notes: 91
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 92: RTC Builderに関する設定
Notes: 92
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 93: RTC Builderに関する設定
Notes: 93
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 94: 独自のデータ型の利用
独自のデータ型でデータポートの通信を行う手順
  IDLファイルを作成する
    MyDataType.idlを任意のフォルダ(ここではC:\UserDefType)作成
    別のIDLファイルをインクルードしている場合は同じフォルダにコピーする
Notes: 94
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 95: 独自のデータ型の利用
独自のデータ型でデータポートの通信を行う手順
  RTC Builderの設定でIDLファイルの存在するディレクトリを追加
Notes: 95
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 96: 独自のデータ型の利用
独自のデータ型でデータポートの通信を行う手順
Notes: 96
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 97
RT System Editor
補足

## Slide 98: コネクタプロファイルの設定
項目 | 設定内容
Name | 接続の名称
DataType | ポート間で送受信するデータの型．ex)TimedOctet,TimedShortなど
InterfaceType | データを送信方法．ex)corba_cdrなど
DataFlowType | データの送信手順．ex)push, pullなど
SubscriptionType | データ送信タイミング．送信方法がPushの場合有効．New, Periodic, Flushから選択
Push Rate | データ送信周期(単位：Hz)．SubscriptionTypeがPeriodicの場合のみ有効
Push Policy | データ送信ポリシー．SubscriptionTypeがNew，Periodicの場合のみ有効． all，fifo，skip，newから選択
Skip Count | 送信データスキップ数．Push PolicyがSkipの場合のみ有効
Notes: 98
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 99: コネクタプロファイルの設定
InterfaceTye
  データの送信方法
  1.1.2ではcorba_cdr(CORBAによる通信)のみ選択可能
  1.2.0では以下の通信方法も選択可能になる予定
    direct(同一プロセスで起動したRTC間でデータを直接変数に渡す)
    shared_memory(共有メモリによる通信)
DataFlowType
  データの送信手順
    Push
      OutPortがInPortにデータを送る
    Pull
      InPortがOutPortに問い合わせてデータを受け取る
SubscriptionType
  データ送信タイミング(DataFlowTypeがPush型のみ有効)
    flush(同期)
      バッファを介さず即座に同期的に送信
    new(非同期)
      バッファ内に新規データが格納されたタイミングで送信
    periodic(非同期)
      一定周期で定期的にデータを送信
Push Policy(SubscriptionTypeがnew、periodicのみ有効)
  データ送信ポリシー
    all
      バッファ内のデータを一括送信
    fifo
      バッファ内のデータをFIFOで１個ずつ送信
    skip
      バッファ内のデータを間引いて送信
    new
      バッファ内のデータの最新値を送信(古い値は捨てられる)
Notes: 99
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 100: コネクタプロファイルの設定
DataFlowType
  Push
  Pull
Notes: 100
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 101: コネクタプロファイルの設定
SubscriptionType
  flush(同期)
  new、 periodic(非同期)
Notes: 101
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 102: コネクタプロファイルの設定
項目 | 設定内容
Buffer length | バッファの大きさ
Buffer full policy | データ書き込み時に，バッファフルだった場合の処理．overwrite，do_nothing，blockから選択
Buffer write timeout | データ書き込み時に，タイムアウトイベントを発生させるまでの時間(単位:秒)
Buffer empty policy | データ読み出し時に，バッファが空だった場合の処理．readback，do_nothing，blockから選択
Buffer read timeout | データ読み出し時に，タイムアウトイベントを発生させるまでの時間(単位:秒)
Notes: 102
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 103: サービスポートについて
コマンドレベルのやり取りを行うための仕組み
  任意のタイミングで操作を行いたい時などに使用
    例えばロボットアームのサーボを停止させる、ハンドを閉じる等
コンシューマ側がプロバイダ側が提供する関数群(オペレーション、メソッド)を呼び出す
インターフェースはIDLファイルで定義する。
Notes: 103
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 104: サービスポートの接続
Notes: 104
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 105: コンフィギュレーションパラメータについて
パラメータを外部から操作する仕組み
  コンポーネント作成後に変更が必要なパラメータを設定する
    例えばデバイスが接続されているCOMポート番号の設定等
Notes: 105
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 106: コンフィギュレーションパラメータの設定
Notes: 106
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 107: コンフィギュレーションパラメータの設定
方法1
方法2
Notes: 107
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 108: マネージャの操作
CameraViewerComp.exe、OpenCVCameraComp.exeのプロセスではマネージャが起動している
  マネージャがコンポーネントを起動する
Notes: 108
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 109: マネージャの操作
Notes: 109
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 110: マネージャの操作
マスターマネージャの起動、RT System Editorからの操作によるRTCの生成までの手順を説明する
  rtc.confの設定
    「manager.is_master」を「YES」に設定して起動するマネージャをマスターに設定する
      manager.is_master: YES
    モジュール探索パスの設定
      manager.modules.load_path: ., C:\\Program Files (x86)\\OpenRTM-aist\\1.1.2\\Components\\C++\\Examples\\vc12
  作成したrtc.confを設定ファイルの指定してrtcd.exeを起動する
    rtcdはコマンドプロンプトからrtcd.exeを入力するか、OpenRTM-aistをインストールしたフォルダからコピーして使用する
    rtcdはマネージャの起動のみを行う
      ～Comp.exeは起動時に特定のコンポーネントの起動も行う
    RT Syetem Editorのネームサービスビューにマネージャが表示される
Notes: 110
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 111: マネージャの操作
モジュールのロード
Notes: 111
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 112: マネージャの操作
モジュールのロード
Notes: 112
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 113: マネージャの操作
RTCの生成
Notes: 113
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 114: 実行コンテキストの操作
Notes: 114
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 115: 実行コンテキストの操作
実行周期の設定
Notes: 115
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 116: 実行コンテキストの操作
実行コンテキストの関連付け
  RTC起動時に生成した実行コンテキスト以外の実行コンテキストと関連付け
    関連付けた実行コンテキストでRTCを駆動させる
  他のRTCとの実行を同期させる
Notes: 116
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 117: 実行コンテキストの操作
実行コンテキストの関連付け
Notes: 117
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 118: 複合コンポーネントの操作
複合コンポーネントの生成
Notes: 118
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 119: 複合コンポーネントの操作
複合コンポーネントの生成
Type
  以下の3種類から選択可能
    PeriodicECShared
      実行コンテキストの共有
    PeriodicStateShared
      実行コンテキスト、状態の共有
    Grouping
      グループ化のみ
Notes: 119
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 120: 複合コンポーネントの操作
Notes: 120
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 121: 複合コンポーネントの操作
Notes: 121
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 122: ゾンビの削除
RTCのプロセスが異常終了する等してネームサーバーにゾンビが残った場合、以下の手順で削除する
Notes: 122
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 123: RT System Editorに関する設定
Notes: 123
At first, I’d like to mention about RT.
What is RT?
RT means Robot Technology.
This is not only standalone robots like this, but also robotic elements, sensors, actuators and so on.
We have studied on RT-Middleware.
RT-Middleware is software platform to integrate these RT-elements.

## Slide 124: How to check the progress
124
Check with Zoom's "Raise Hand Button"
Display the participant's screen.
Raise your hand if there is a problem
If it is resolved, lower your hand
Notes: 124
We may check the progress during the training.
If you have any trouble, please use raise hand button.